## Slide 1: How do drivers judge speed?
Peripheral vision
Height above the road
Familiarity
Complexity of the scene
Noise level
Adaptation effect
Perceptual Cues:
Notes: Source “Driver Speed Estimation: What Road Designers Should Know” 1999. http://www.hfn.ca/driver.htm
A driver’s main cue for speed comes from peripheral vision. When peripheral vision is eliminated, and drivers use only the central field of view to determine speed, ability to estimate actual speed is poor. This is because the view changes very slowly in the centre of a road scene. If, on the other hand, the central portion of the road scene is blocked out, and drivers are asked to estimate speed based on the peripheral view, they do a much better job (Salvatore, 1968). It is the streaming of information in peripheral vision or "optical flow" that most influences our estimates of speed. Consequently, if peripheral stimuli are close by, then drivers will feel they are going faster than if they encounter a wide open situation. In one study, drivers were asked to drive at 60 mph with the speedometer covered. In an open-road situation, the average speed was 57 mph. After the same instructions, but along a tree-lined route, the average speed was 53 mph (Shinar, McDowell and Rockwell, 1974). The trees, close by, provided peripheral stimulation, giving a sense of higher speed.
Another cue to speed is the height of the eye above the road. The closer the driver is to the road, because of the geometry of the situation, the higher the angular velocities appear to be, and so the greater the sense of speed. A given speed feels faster in a sports car than in a truck simply because of being closer to the roadway.
On curves, there are kinesthetic cues. A driver who is familiar with a curve will have previously experienced its lateral acceleration. The greater the lateral acceleration, the stronger the "seat-of-the-pants" feel and the slower the driver will take the curve. Unfamiliar drivers have to rely on the appearance of the curve. They have to look at the radius, the angle the curve goes through, lane width, and sight distance. Ideally, the driver would rely on the radius, because that is what predicts the lateral acceleration which is what determines the most appropriate speed. Unfortunately, a study where people were asked to estimate speeds by looking at roadway scenes found that they were much more influenced by the curve angle in estimating the appropriate speed (Fildes and Triggs, 1985).
A complex visual scene gives a greater sense of speed than a visually impoverished one. One explanation offered for inappropriate speeds in fog is the absence of peripheral stimulation. To increase optical flow in peripheral vision to a more normal level, some drivers speed up.
Noise level is also an important cue to speed. There have been a number of studies of the impact of removing noise cues by putting earmuffs on drivers, or by attenuating sounds in other ways. The result is that drivers underestimate how fast they are going and drive 4 to 6 mph faster to obtain the same speed that they had when the sound cues were present (Evans, 1970(a)(b)). With respect to lowering speeds, it has been counter-productive to progressively quieten the ride in cars, and to provide smoother pavements. This just decreases drivers’ sensitivity to their own speed.
Most drivers are aware of the adaptation effect. This is the experience of leaving a freeway after a long period of driving, and having difficulty conforming to the speed limit on an arterial road. One study required subjects to drive for 20 miles on a freeway and then drop their speeds down to 40 mph. The average they were able to achieve was 50 mph (Schmidt and Tiffin, 1969). This was still too high despite the fact that these drivers were perfectly aware of this adaptation effect, told the researchers they knew this was happening, and tried to bring their speed down. This adaptation effect was shown to last up to 5 or 6 minutes after leaving a freeway and to happen after very short periods of high speed, as little as 5 seconds. Drivers had adapted and did not realize how fast they were going, even after a short burst of speed.

## Slide 2: Hampton Roads Tunnel
Notes: The Hampton Roads Tunnel between Hampton and Norfolk, VA is a good example of this concept. Highway officials understood that drivers in this tunnel had a tendency to slow down while driving through and posted signs that read, “Maintain 55 mph”

## Slide 3: Monument Ave. – Richmond, VA
Wide Median
Street Parking
Cobblestone
Surface
Trees
Notes: <number>
<footer>
<header>
<date/time>
Identify four things on Monument Ave. that can alter a drivers perception of speed:
The overhanging trees cut down on the driver’s peripheral vision.
The wide landscaped median narrows the road on the left.
The on-street parking narrows the road on the right.
The rough surface creates rougher, noisier ride.

## Slide 4
Lane Narrowing/Pavement Markings
Notes: Slide transition shows how changes in pavement markings can narrow this street and reduce speeds

## Slide 5: Lane Narrowing/Pavement Markings
Parking
Bike Lane
Left Turn Lane

## Slide 6: Centerline and Edgeline Striping
Goal is to visually narrow the street
Mixed results
Bicycle lanes might have more effect than just centerlines or edgelines (painted lines several feet in from curb)
Bike lane
striped
Centerline
striped
Notes: <number>
<footer>
<header>
<date/time>
Source: City of Sacramento Public Works website, www.pwsacramento.com/traffic
Some cities, such as Sacramento, CA operate a two phase traffic management program. If communities request it, they begin with the first phase, which includes less restrictive measures, such as centerline striping, bike lanes, parking lanes, and speed limit signs. Phase II is used if traffic concerns persist and these measures include more restrictive and expensive approaches such as traffic circles, chokers, and speed humps.

## Slide 7: Chevrons & Transverse Bars
Notes: One of the more successful techniques has been the use of progressively closer transverse lane markings - horizontal bars across the pavement that get closer and closer and give the sensation of going faster and faster. These have been applied at different locations in England at roundabouts, and in Canada, at the end of freeway ramps. A similar technique used in Japan involves converging chevrons that get progressively closer.
Generally, the effect is the same. There is an immediate reduction in speed and, in particular, in the prevalence of higher speeds, but the effect disappears fairly rapidly (Griffin and Reinhardt, 1996). Here, the perception of the road is changed, but the actual demand of the roadway has not. Changing the perception will have an effect on the first-time driver, but not on the person who drives that route every day and soon realizes that nothing has really changed in terms of the driving task.
Source “Driver Speed Estimation: What Road Designers Should Know” 1999. http://www.hfn.ca/driver.htm

## Slide 8: Re-enforcing Lane Markings to Influence Drivers
Less Noticeable Edgeline
Rumble Strip
Wide Centerline
Notes: Example: Research carried out in the Netherlands addressed the problem of slowing drivers on 80 km/h roads, particularly near village entry points. Researchers decided on a continuous rumble street edging treatment, which effectively narrowed the comfortable lane width. This would increase the difficulty of the driving task and thereby achieve the goal of slowing drivers. It did not reduce recovery area, which would affect safety, as it did not narrow the actual lane width. There was still room to maneuver if necessary. However, the researchers were concerned that the rumble strip edging treatment might result in drivers moving over towards the oncoming traffic. Indeed it did do that. To offset this tendency the centre line delineation was widened to increase its conspicuity, and the conspicuity of the edge line delineation was reduced. A before-after study using comparison control sites found a 20% reduction in accidents after a 2-year period.
Source “Driver Speed Estimation: What Road Designers Should Know” 1999. http://www.hfn.ca/driver.htm

## Slide 9
 Murray Ridge
Notes: Video Clip- 2:41 This video segment, entitled “Murray Ridge Road” shows Officer Tony El-Assis of the San Diego (CA) Police Department. The video shows a wide residential street that area residents used as a cut through to avoid signal lights. Speeds averaged 49 mph in the 35 mph zone. Officer El-Assis turned the 4 lane street into a 2 lane street, one in each direction, striped in bike and parking lanes, and added in 2-way left turn pockets, all of which narrowed the street slowing speeders to 35 mph average. The instructor can ask the class, “What else might have worked to turn the speeding problem on this street around?”

## Slide 10
2-way southbound
2-way northbound
Foothill & Loring - Before
Loring
Foothill
A hill
Notes: <number>
<footer>
<header>
<date/time>
Exercise- present this problem to the groups and ask them how they could change these streets to reduce speeding.
Foothill is residential street
Loring is feeder road to the beach
Speeds on Foothill in excess of 45 mph
Residents can’t back out of their driveways
Then show them the actual changes and follow-up with the video clip.

## Slide 11
Foothill & Loring - After
1-way southbound
Bike lane
1-way northbound
Turn lane
Deflectors
Loring
A hill
Foothill
Notes: <number>
<footer>
<header>
<date/time>
Changes:
Stop sign replaces right turn yield sign on Loring
Bike lane added to Foothill southbound
Southbound Foothill reduced from two lane to one lane
Left turn lane added on Foothill turning on to Loring
Northbound Foothill reduced from two lane to one lane
Deflectors added to Loring former right turn lane to encourage stopping before turning right onto Foothill.

## Slide 12
 Foothill & Loring
Notes: Video Clip- 3:13 Information on engineering changes to these streets to promote safety and reduce speeds.

## Slide 13: Melrose Avenue
6,500 cars per day on this residential street
Cars speed as they wind downhill
40 mph average speeds
Citizen conflict over 4-way stop sign
Parking lane can be added as was done at the top of the hill
Notes: The following clip illustrates how this problem was handled.

## Slide 14
 Melrose Ave.
Notes: Video Clip- 3:20 Addresses Stop signs, narrowing, and citizen input.

## Slide 15:  Corral Canyon
Notes: <number>
<footer>
<header>
<date/time>
Video Clip- 1:24 Agent Steve Guthrie of the Chula Vista (CA) Police Department describing a traffic calmed street that a California Highway Patrol Officer put in place. The video shows a traffic calmed street that is 2 miles long. The roadway was approximately 70 feet wide, too wide for a residential street.

## Slide 16: Comparison of Costs
$40,000
$40,000
$40,000
0
$145,000
$214,000
$194,000
$30,000
$85,000
0
$70,000
$300,000 ($2,000 per hump)
Photo-Radar (ownership option)
Photo-Radar (leased option)
Targeted Police Enforcement
Speed Humps
Revenue
Annual Cost
Initial Cost
Measure
Notes: <number>
<footer>
<header>
<date/time>
These cost comparisons are drawn from Traffic Calming: State of the Practice (1999) (pp. 116-126).

## Slide 17: Designing Out Speeding in New Developments
Some growing communities require developers to design new residential areas to prevent traffic problems
Some features might include narrower streets, roundabouts for high volume areas, and sharp bends and other “slow points” at regular intervals
Some cities are designing residential streets as narrow as 18 feet
Notes: <number>
<footer>
<header>
<date/time>
Traffic Calming: State of the Practice (1999) (chapter X).
Class questions:
Compare the street width in video segments Ocean Hills and Otay Ranch

## Slide 18:  Ocean Hills
Notes: <number>
<footer>
<header>
<date/time>
Video Clip- 1:08 Sgt. Joe Snarponis of the San Diego (CA) Police Department. The next slide shows his approach to countering speeding. The last bullet on the next slide is a question that the facilitator can have the class discuss.

## Slide 19: Ocean Hills Neighborhood
Residents surveyed, speeding was top of the list of community complaints
Officer Snarponis and his lieutenant conducted follow-up interviews with residents
Entrance street to neighborhood more than 100 feet wide. Downhill slope as residents exit exacerbates the speeding problem
Police should review plans for new developments
What could be done to slow speeds of residents exiting this neighborhood?

## Slide 20:  Otay Ranch
Notes: <number>
<footer>
<header>
<date/time>
Video Clip- 1:37 Agent Steve Guthrie of the Chula Vista (CA) Police Department touring a new development, Otay Ranch, where the design of the development limits speeds. The last frame of the video segment asks the class to “list all the traffic calming approaches used in this development.” The class should be able to describe each and discuss how the approach reduces speeds. They include:
Defined entrance to neighborhoods, signaling drivers that they are entering a residential area
Narrow streets
Community developed for use by electric vehicles (which can’t go over 25 mph)
Center parks act as large traffic circles slowing drivers down because they have to make turns
Smaller traffic circles dot the neighborhood
Overall design limits speeds of vehicles

## Slide 21:  Neighborhood Speeding Problem
Notes: <number>
<footer>
<header>
<date/time>
Video Clip- 0:58 This video segment shows a street. As the camera travels down the street, the following question scrolls onto the screen, “What would you do to minimize speeding on this street?” The facilitator should try to elicit responses from the class. Ask them to start from the beginning, not just jump to engineering or enforcement. Show the slides that follows after the class has assembled a list of things it could do and check it against the class’ responses.

## Slide 22: Addressing Speeding Problems A Sample Process
Interview complaints to determine:
  if there is really a speeding problem,
  the times of day, and days of week, it occurs, and if
  there are certain people who are the worst offenders?
2. Conduct speed survey to determine the 85th percentile
  Train police volunteers to conduct speed survey
  Review the survey data to determine if there is a speeding problem
Notes: A sample process to follow when faced with speeding complaints.

## Slide 23: Addressing Speeding Problems A Sample Process
3. If there is not a speeding problem:
  show the survey data to community members
  have community members watch you conduct radar to show them that speeding is not occurring
If a speeding problem exists, do a visual assessment of the street to look for contributing factors:
  street width?
  downward slope?
  is the street being used as a cut-through?
  signage appropriate to the street?

## Slide 24: Addressing Speeding Problems A Sample Process
Hold a community meeting to discuss results of the speed survey and discuss alternatives and the effectiveness of each alternative:
  education
  enforcement
  regulation
  engineering

## Slide 25: Summary

## Slide 26: Speeding Approaches – Summary
Education
Enforcement
Regulation
Engineering
Neighborhood
Safety
Campaigns
Radar &
Photo Radar
Stop Signs
& Speed
Limit Signs
Traffic
Calming
Speeding Complaint
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27
Physical
Chokers
Pinch-points
Engineering
Traffic
Calming
Self-
Enforcing
Chicanes
Traffic Circles
Roundabouts
Speed Humps
Speed Tables
Psycho Motor
Parking Lanes
Bike Lanes
Horizontal
Narrowing
Techniques
Vertical
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28:  Palm Ave.
Notes: <number>
<footer>
<header>
<date/time>
Video Clip- 2:43 This video segment, entitled “Palm Avenue” shows Sgt. Joe Snarponis in front of Palm Avenue, a 6-lane arterial street. The street, about 1/8 of a mile long, is dotted with mobile home trailers, and has signal lights at either end. The street feeds into a major freeway. This one block of Palm Avenue is home to over a 1,000 residents residing in the mobile homes. Residents cross the 6-lane roadway at mid-block rather than walk to the signal lights at either end. Cars speed up between signals and travel at high speeds. In one 18-month period, motorists killed 5 pedestrians in separate crashes on this block. The video shows Sgt. Snarponis’ response to the problem for which he received community support. This video is a good example of a very serious, and tragic problem can be turned around by one officer. One of the most important things that Sgt. Snarponis suggests is not to assume when you are working with other agencies, that they have accurate and up-to-date information. While, in this case, Sgt. Snarponis had to convince Caltrans, the state transportation agency, to do something about the problem, in many cases, police officers have to convince their local traffic engineering agency, and that agency may not have all of the information it needs to make a good decision. Information that police may need to provide to the local traffic engineering department includes:
the number of accidents
Injuries
The extent of speeding enforcement efforts thus far
The amount of time already committed to trying to reduce the speeding problem on the street or roadway
The extent of community support for something else to be done.

## Slide 29: So remember…
Residential speeding, it’s a common problem
It’s important to know the specifics of the street you want to impact
It’s important to know what approaches work and for how long
You have options in impacting it
Measure whether or not what you did worked. Did it reduce the speeding problem? If so by how much?
Notes: <number>
<footer>
<header>
<date/time>
Instructor Notes: This is the last slide in the powerpoint. Feel free to add others as needed. For information or questions about this powerpoint or the video segments that accompany it, email Dave Maddox at dmaddox@vcpionline.org or call 804.644.0383.

## Slide 30
Do you know how fast you were going?
"The significant problems we face cannot be solved at the same level of thinking we were at when we created them."
-Albert Einstein
www.vcpionline.org

## Slide 31
Thanks!